## Slide 1: An Application to Optimize Lap-times for Race Cars
Group Members: | 
Alaa Bashir | ge73cec
Ankit Khot | ge73xuq
Máté Kelemen | ge49pil
Supervised by: Jan Janse van Rensburg and Steve Schäfer | 

## Slide 2: Outline:
Recap
Introduction to point mass model
Literature Review for vehicle dynamics
Point mass dynamics
Controller Design
Summary

## Slide 3: Recap
Goal :
To minimize total lap time
Problem Statement :
Dual problem
So far :
Geometric Optimization
Interface to 3D Engine(UNREAL+Simulink)
A Question from last session :
Order of Optimization (fmincon MATLAB function)

## Slide 4: Milestones
Literature Review
(Optimizing the path)
Controller controlled Vehicle in Unreal engine
Finding Optimum path for a point mass
Familiarize ourselves with MATLAB and Simulink
Literature Review
(Vehicle dynamics constraints)
Finding Optimum lap time for a point mass
Start

## Slide 5: Milestones
Extending point mass model for single track and double track models
Generalizing the model for different race tracks

## Slide 6: Introduction : Point Mass Model
Considers vehicle as a point mass
Dynamics of the point mass model:
Acceleration : a
Weight : mg
Height of CG from ground level : h
Overall friction coefficient : 𝛍
Frictional force, F frictional : 𝛍mg
Centripetal force, Fcentripetal :
Vcritical = (Sliding) OR
Vcritical = (Overturning)
Notes: Point mass models
Double dots

## Slide 7: Vehicle Dynamics : Literature Review
Vehicle Models :
Single Track Model :
  3 DOFs : Longitudinal, Lateral and Yaw
  Does not consider the rolling effect
Double Track Model :
  6DOFs : Longitudinal, Lateral, Vertical
  Yaw, Roll, Pitch
These models involve modelling of
the Tire, Suspension system, Chassis,
Transmission system etc.
Simulink : Reuse of the Simulink Vehicle Dynamics Block set.
Image source : Automotive engineering, systems and dynamic behavior by Pablo Luque.
Notes: Expand on Simulink – reuse Simulink libraries (vehicle dynamics blockset)
+ slide for Simulink model screenshots – check documentation

## Slide 8: MATLAB Implementation (PM dynamics)
Select optimization target
Define dynamics
Optimization
Process path (,L)
Dynamics (a,v,)
Preconstraining
Notes: Optimization( geometric(total length, curvature), lap time )
-> if lap time, we need the dynamics (infinite acceleration, rate limited acceleration, RL+brake checking )
Process track -> get curvatures, length, … (geometric properties of the path)
Preconstraining (calculate max velocities for every point, apply brake checking )
Dynamics -> calculate accelerations,velocities -> total lap time
Optimization algorithm gives us a new path

## Slide 9: Point Mass Dynamics
Dynamics
Infinite acceleration
Notes: Point mass models
Double dots

## Slide 10: Point Mass Dynamics
Dynamics
Rate limited acceleration
Notes: Point mass models
Double dots

## Slide 11: Point Mass Dynamics
Dynamics
Rate limited acceleration with break checking
Notes: Point mass models
Double dots

## Slide 12: Point Mass Dynamics
Lap times [s] |  | Optimization target |  | 
 |  | Length | Curvature | Time
Model | Infinite accel. | 15.08 | 16.54 | 13.66
 | Rate limited* | 15.76 | 16.85 | 13.14
* Starts with maximum velocity
Notes: Change to a full track
More details and parameters + which model we’re using
Time/average speed, 3 results for different paths
Initial velocity for the rate limited model

## Slide 13: Controller Design Roadmap
Test case creation
Build a control system
Testing and Visualization

## Slide 14: Test Case Creation
Using “Driving Scenario Designer” App to get:
  Reference position
  Road curvature
  Speed Profile
  Direction

## Slide 15: Control System

## Slide 16: Control System
Output of the Driving Scenario Design

## Slide 17: Control System

## Slide 18: Control System
Lateral Controller
Longitudinal Controller

## Slide 19: Control System

## Slide 20: Control System

## Slide 21: Testing and Visualization
Using Vehicle XY Plotter

## Slide 22: Controller Evaluation
Position Error
Relative Heading
Velocity Error

## Slide 23: Summary
Recap
Literature Review for vehicle dynamics
MATLAB Implementation
Controller Design in Simulink

## Slide 24: References :
A Vehicle Dynamics Model for Driving Simulators - Jorge Gómez Fernández
An overview on vehicle dynamics - Shaopu Yang, Yongjie Lu, Shaohua Li